CHI TIẾT SẢN PHẨM

| UPS MODEL |  | HL-3C20KS |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Rated capacity | 20KVA/16KW |  |  |  |
| INPUT |  |  |  |  |  |  |
| Wire method | Single phrase or three phase earth ground |
| Rated voltage | 380VAC |  |
| Normal Voltage | 120VAC - 275VAC ±5 |
| Rated Freq | 50HZ |
| Frequency Range | (45- 55)HZ±0.5HZ |
| Bypass range | 187VAC-264VAC |
| BAT |  |  |  |  |  |  |
| Rated bat Voltage | 192VDC |
| Battery capacity*Quantily | 12VDC*16PCS |  |
| AC OUTPUT |  |  |  |  |  |  |
| Output system | Single phrase & earth ground |
| OutPut voltage | 220VAC±3% |
| Output frequency | 50HZ±1% |
| Dynamic voltage transient range | <5% |
| Dynamic transient restore | <60ms |
| Waveform | Sine ware THD<3%(linear load) Sine ware TDH<8%(nonlinear load) |
| Input power factor | 0.8 |
| Overload capability | 105%-125% 30s to Bypass |
| Communications | RS232(turn to 485), Intelligelt slot |
| Net weight |  |  |  |  |  |  |
| Dimensions | 248*500*616mm |  |
| Environmental |  |  |  |  |  |  |
| Ambient temperature | 10ᵒC - +40ᵒC |
| Altiude | Lower than 1000m: no derating Over 1000m: 1% derating for every 100m rise |
| Storage temperature | 15ᵒC - + 45ᵒC |
| HL -UPS ONLINE TỪ 6KVA - 20KVA ĐƯỢC BẢO HÀNH 36 THÁNG CHO BỘ XỬ LÝ VÀ 24 THÁNG CHO ẮC QUY |